## Slide 1
What is the next step of YANG effort in IETF: Service Oriented YANG Pilot Project?
Qin Wu
Huawei

## Slide 2: Where we are for YANG adoption in Industry
EANTC launched NETCONF/YANG Multi-vendor Interoperability Test starting from 2016, Test every year since 2016,
The main use cases :L3VPN service provision, L2VPN service provision.
Addition Use cases (2023): NETCONF transport slicing, system inventory, routing policy configuration
The referenced IETF models : L3SM,L2SM, Network slicing service model in TEAS WG, etc
Opeconfig YANG, Native YANG and IETF YANG at device level;
Observation 1: Slow Adoption
Of Device Level YANG
Observation 2: Fast Adoption of
Service/Network Level YANG

## Slide 3: IETF YANG Model Standardization Journey
100+ YANG data models developed by Open Daylight
YANG data model considered in Most of protocol specific WGs in Charter
Routing Management YANG -> foundation for all routing protocol models
2014 YANG Takes Off in Industry
RFC8969 guidance for YANG integration at different level
L3NM and L2NM Design Team Work
IETF Network slicing design team formed
YANG versioning DT is setup around May, 2018
Slow adoption of Device Level VPN YANG such as EVPN, L2VPN,L3VPN and QoS
2019~2021 SDN NBI continue to grow interests，Slow adoption of IETF SBI YANG
Camara NaaS was Launched at MWC at Feb 2022
Service assurance and monitoring model gets attraction such as Service assurance YANG, VPN PM YANG, SAP YANG, Attachment Circuit, etc
Model versioning for individual YANG matured, YANG package ongoing
Some leading operators experiment IETF YANG using open source or PoC project
2022~ Now Where we are now YANG adoption Catalyst
L3SM/L2SM WGs
LIME,I2SNF WGs, and ACTN
Network Slicing BOF coordinated with 3GPP and pushed back a lot
Each WG in routing area creates protocol specific YANG design team
Routing YANG Architecture Design Team setup to align with Openconfig and was closed down in 2018
IETF YANG Coordination Group was formed to provide tooling and coordination within IETF
YANG Catalog were kicked off to Provide tooling and easy use way to find YANG models
2014~2018 SDN NBI/SBI YANG Flourishes
Service Level/Network Level
YANG Model Work
Device Level
YANG Model Work

## Slide 4: Challenging and Issues of Implementing YANG
Gap with Industry needs
  Many operators are not engaged enough in the IETF to create that perfect world.
    Except Service model work
    Operators has more voice in opensource community, e.g., Openconfig
    Slow IETF process makes technology integration lengthy
  The operators expected to deploy these technologies often don't even know that the standards are being developed.
    YANG Catalog and provide visibility to IETF YANG and makes difference a lot
  The operators who know that the standards are being developed may not know how these models work together to configure a device, manage a set of devices involved in a service.
    No Service Oriented Cook Book
    YANG Integration Samples
This lead to critical new technologies currently being developed without sufficient direct operator input.

## Slide 5: What have already been done with IETF YANG
SDN Controllers
SBI
Orchestrator
NBI
APP
APP
APP
NBI
Customer
OPSAWG WG
TEAS WG
Fundamental
NETCONF WG
PCE WG
L2/L3SM WG
I2RS WG
BESS WG
L3VPN/EVPN/L2VPN
YANG Language
NETCONF/RESTCONF
PCE Protocol
L2/L3VPN/VN/TE Service Mapping
Architecture, Generic TE Models
Generic Network Topo Models
NETMOD WG
L2NM,L3NM, UNI Top Model
L3NM
L3SM
IDR WG
BGP Policy and BGP-LS
Phase 1: Engaging Operators: Develop Service Level API related YANG Data
Model Work, such as L3SM, L2SM, I2NSF; Develop Generic Policy YANG Model
that works at different level such as SUP
Phase 2: Setup YANG Catalog to provide a reference for all YANG modules
available in the industry
Phase 3: YANG Model Integration Guide: Develop model driven automation
framework to provide guidance For building fully automated YANG based System;
Phase 4: Develop Network Level API related YANG data model such as L3NM
,L2NM, Network Slicing, SAP(Service Attachment Point), VPN NBI PM, etc
Phase 5: Setup Service Driven YANG Pilot project to catalyze YANG adoption
In the industry:
Network Inventory Initiative looking for alignment with different SDOs and
Open source project
Teraflow Transport Controller Project driven by Telefonica
Data Mesh open source project driven by Swisscom
SRv6 Visibility Project driven by Swisscom

## Slide 6: Application and Network Collaboration among telco operators, vendors and hyperscalers
Our understanding of CAMARA
Carriers & Vendor joint activities
1
3
Use Case Catalog(planning)
Service API Practice
Network API Implementation
“0-Touch” 5G Mobile ATM Services
Mobile Game Acceleration
Download Acceleration Services(BoD)
Mobile Device location
Autonomous Network UC
NFs + NEF APIs
5G Slicing + Network APIs
Network API Standardization
Developers and Product Manager User Story
Service API joint-Definition
Use case Scenario
Service Applications
Network Resources
MBB
Quality on Demand
Device Location
Device Status
FBB
Home Devices Quality on Demand
Optical private line Quality on Demand
NEF
Controller
Controller
Controller
Controller
4/5G Radio & Core
Transport (Optical，IP)
ACCESS
Unified and E2E Service Orchestrator with API exposure
Network API (IETF, BBF, IEEE, TMF)
Service API
Autonomous Network
Service API Gateway
Transform Function
Network API Gateway
Camara NaaS was Launched at MWC at Feb 2022 and Operated for one year.

## Slide 7: Model Correlation Relationship Overview
IETF Network Model
IETF Network Topo Model
Network Inventory
Model
Network Device
Model
L3 Topo
L2 Topo
TE Topo
DC Fabric Topo
SAP/UNI Topo
Network Performance Monitoring
L3NM
L2NM
NRP
L3SM
L2SM
IETF Transport Slice Service
IETF Attachment Circuit Network Model
IETF Attachment Circuit Service Model
IETF Bearer Service Model
TE Tunnel
TE Tunnel Telemetry
Network Slice Topo
BGP
OSPF
ISIS
RIB
L3VPN
L2VPN
EVPN
MVPN
ACL
QoS Policy
Routing Policy
BFD
IPFIX
TWMAP
IOAM
BMP
TE Service Mapping
TE VN Model
Device Level Models:
Network Level Models:
Service Level Models:
OAM/PM:
Policy Layer:
Routing Layer:
Service Layer:
L1CSM
SR
Policy
SR/SRv6
Slice Service Mapping
Augment
Augment
Augment
Mapping
Mapping
Mapping
Mapping
Mapping
Augment
Orchestrator
Controller
Orchestrator
Service Level Model
Network Level Model
Network Level Topo Model
Device Level Model
Correlation via Augment
Correlation via Mapping
Fulfill
Assurance
Notes: This slides show the whole picture of Network Inventory. In this picture, not only we can see Network Inventory models but also we can its periphery neighboring models, These models can be break down into three level models, Service Level, Network Level and Device Level.
Network Inventory is placed in the NBI of SDN controller together with Network Level Models such as L3NM, L2NM.
In addition, we see, model relation can be established using correlation, there are two type of correlation, one is correlation based on augment,
The other is correlation based on mapping.
Typical example of correlation based on augment is network model defined in RFC8345 has been extended for L3 topo, L2 topo and network inventory.
Typical example of correlation based on mapping is we define a separate model,e.g., TE service mapping to map L3SM into TE Tunnel or VN model. We also can not define explicit dependency relation between service model and device model, let vendor or operators themselves decide.

## Slide 8: Network Device Anatomy
System Inventory Object Layer
System Management Layer
Network Resource Layer
Network Policy Layer
Network Protocol Layer
Network Service Layer
Network
Device
Device Mgmt
Logical System Mgmt
System Component Mgmt
System Info
Software Install&Update
System Process Monitoring
Interface Mgmt
Tunnel Mgmt
QoS Queue Mgmt
Topo Mgmt
ACL
QoS Policy
Routing Policy
Security Policy
SR/SRv6
BGP
OSPF
ISIS
L3VPN
L2VPN
EVPN
SDWAN
5G Slicing
Network Device YANG Logical Organization
Source: https://datatracker.ietf.org/doc/html/draft-ietf-rtgwg-device-model-02
Network Device (Physical or Virtual)
Network Infrastructure
Network
Instance
Network
Instance
Network
Instance
Network
Instance
Network
Instance
Network
Instance
Logical Network Element
Logical Network Element
Interfaces
Interfaces
Service Plane
(Data Plane/Control Plane/Management Plane)
Sample Network Device Architecture Design
Configuration Data Layering
Software
And hardware
Inventory Data
YANG configuration data Container
BGP
OSPF
ISIS
RIB
L3VPN
L2VPN
EVPN
MVPN
ACL
QoS Policy
Routing Policy
BFD
IPFIX
TWMAP
IOAM
BMP
SR
Policy
SR/SRv6
Notes: So what is inside of network device. I think we can break down network device related data into multiple layers, e.g. service layer, protocol layer, policy layer, system management layer, system inventory object layer. In these layers, the bottom two layer related to network infrastrucuture,
Clearly distinct with other layers in the control plane, forwarding plane and management plane.
Also we can refer to Network Device Model defined in RTGWG WG which never get published. But it provide encapsulation layer or envelop layer to organize configuration model at the device layer together. The encapsulation layer include logical network element which is related to vRouter, vfW.

## Slide 9: Network Inventory Functional Overview
Basic Network Inventory Functionalities
Physical Location Management
Geo Location Management
License Management
Network Element Management
Logical Element Management
Hardware Component Management
System Software Component Management
Application Software
Files
IP address/Prefix Pool
RD Pool,etc
Logical Network Inventory
……
Physical Port Management
Physical Connection Management
VLAN Pool,etc
In scope of IVY WG
Beyond scope of IVY WG
Zone List/Region List,etc
Notes: Here is the Network Inventory Function view, based on Network device anatomy, we can see the network inventory MUST include
Both physical network element but also logical network element, in addition, it include physical hardware component, but also
System software component, what is not in the scope of IVY include application software, Files, IP address pool which are more related
To logical network inventory data.

## Slide 10: Basic Network Inventory vs Logical Network Inventory
Logical Network Inventory
Service Layer: RT, RD, BGP Community, VRF, BSID, etc.
IP Layer: IP address Pooling, loopback interface, Trunk interface, Device Role, src address, dst address, DSCP, VLAN ID, Sub interface, Zone list, etc.
Basic Network Inventory
Software components: firmware image, OS, bootloader, etc.
Hardware components: processors, memory, physical port, optical module
Network Infrastructure: Network Element such as Router, Switch and Endpoint Device such as PoE device, Camera, etc., or Fiber Optical Cable?
Physical Location and Position: Geo-location, Room, Shelf, Rack, etc.
Tunnel Layer: VXLAN Tunnel, SRv6 Tunnel, TE Tunnel, GRE Tunnel, Gene Tunnel, etc
Application Layer: Application software Name, file name, etc.
License Information: Expiration date, issue date, license id
Policy Layer: Tunnel Policy Profile, QoS Policy Profile, Route Policy Profile etc.
Notes: So we can break down Network inventory into basic network inventory and logical network inventory. Logcial Network inventory
Can also break down into multiple each layer, the key element in each layer is resource Identifier such as IP address, VLAN or the number of specific resource e.g, the numbe of IP addresses in IP address Pool.

## Slide 11: How can we do better for network operators and Developers
Within IETF, Continue to create dedicate working group to define common building block which can be reused in different SDOs, open source projects E.g., Network Inventory to align with ONF, ITU-T SG15, Openconfig
  E.g., Network Attachment Circuit to align with ORAN and look for it be reused by L3SM/Network slicing service model work
  E.g., YANG Package Versioning work
Externally, more open source projects driven by operators to adopt and verify IETF defined YANG data model and look for missing pieces
  collaboration with Camara NaaS API projects
  more open source automation tool and documentation to be public available

## Slide 12: How can we do better for network operators and Developers
Coordinate with BBF, IEEE, MEF, 3GPP, ETSI for data modeling work
  Another IAB workshop on Data model integration and deployment Update
    Coordinate requirements and support for existing SDOs developing standards relevant to YANG
    Discuss YANG model fragmentation at the device level such as IETF YANG, Openconfig YANG, Native YANG
    Explore the limitation and restriction of existing YANG modelling language
    Explore How IETF YANG, and other SDO YANG are related to CAMARA NAAS API
    Investigate automation tool for DSL modelling translation, e.g., mapping NGSI-LD into YANG
    Look for new modeling technology, e.g., Knowledge modelling using RDF