## Slide 1: A YANG Data Model to use device models in the North-Bound Interface of SDN controllers
draft-xxx-device-models
IETF 117 San Francisco
Oscar Gonzalez de Dios, Victor Lopez

## Slide 2: Outline
Introduction
Use cases
YANG model details
Conclusion and future work

## Slide 3: Introduction
There is value in the management and configuration of network elements network-wide.
There are several organizations that can access the device models and they are reusable since the device configuration does not change.
IETF has done a relevant effort to define device models to manage the network element capabilities.
SDN controllers are positioned between OSS and network elements.
There are scenarios where it would be useful to reuse the device models in the NBI of SDN controllers to enable the usage of IETF device models.
+-----+ +------+
| OSS | | Orch |
+-----+ +------+
| | NBI
v v
+----------------+
| SDN Controller |
+----------------+
| | | SBI
v v v
+-----+ +-----+ +-----+
| NE1 | | NE2 | | NE3 |
+-----+ +-----+ +-----+

## Slide 4: Use cases
Profiles. Device models can be used for configuration creation. These profiles can be applied to one or several network elements in the network afterward.
  Link it with profiles in service models
Configuration service. OSS may want to use device models to configure network elements via an SDN controller. The SDN controller enables the configuration service for a network element. Example: ACL or routing policies configuration

## Slide 5: YANG model details
module: foo-ntwdev
+--rw devmod-list* [devmod-name]
+--rw devmod-name string
+--rw foo? -> /foo:foo
+--rw deployment
+--rw network-elements* [ne-id]
+--rw ne-id string
+--rw devmod-alias? string
+--rw grp-network-elements* [grp-ne-id]
+--rw grp-ne-id string
+--rw devmod-alias? string
foo.yang can be any device model.
Defines a list called foo-list with the following elements:
  A leaf named devmod-name of type string that serves as the key/identifier for the list entry
  A leaf named foo that uses a leafref type to reference the foo leaf from the imported foo.yang module
  A container named deployment that includes:
    A list called network-elements with the following elements:
      A leaf named ne-id of type string that is the key/identifier
      A leaf named devmod-alias of type string that serves as the device module alias for the deployment
The YANG model foo-ntwdev primarily creates a list of instances referencing the foo.yang module and provides a nested structure to store deployment information for network elements associated with each instance in the list.

## Slide 6: Conclusion and future work
This is an initial work
Feedback on the proposal to see if there is interest in the WG.